## Slide 1
ESRF Vacuum Control System
Pascal Verdier
ISDD software group
4th of October 2010
Software Vocabulary
ESRF Accelerator Control System
TACO / TANGO
ESRF Vacuum Control System

## Slide 2
Class:
  A class is a software object modeling an object with an interface.
  Assembling classes as bricks will build a software program.
  In our control system, a class models a concrete object
  e.g.: a gauge, a controller, a serial line,…
  And the interface is defined by commands, attributes, properties,…
  It can also model an abstract object (e.g.: beam position or emittance)
Software Vocabulary
Device:
  A device is an instance of a class. e.g.: pump1, pump2, pump3,…
  All devices of a class have the same commands, attributes, properties.
  Only the property values can be different to configure it.
Device Server:
  A device server is a process running on a machine containing one
  (or several) class(es).
  It takes the device and class list from the database.

## Slide 3
Software Vocabulary
Client:
  A client is a remote software object connected on a (or several) device(s)
  It takes the device connection parameters from the database.
  It could be an application, a calculation program or a device (higher level).
Device oriented control system:
  Taco and Tango are device oriented control systems.
  That means :
    Objects known by clients are devices and a device name must be unique.
    Devices are seen as a black box, and all actions (get/set) are done by the interface.
    All devices have the same interface:
      A set of Commands
      A set of Attributes
      A set of Properties
      A set of States
Taco/Tango Convention:
  A device is defined by 3 fields domain / family / member
    domain : e.g.: sr, sy, id08,…
    family : e.g.: d-ct, v-pen,… (should represent the device class).
    member : e.g.: 1, 2, c01-1, … (make unique the device name)

## Slide 4
Software Vocabulary
Class A
Device
D1
Class B
Device Server
Device
D2
Device
D1
Device
D2
Client
Client
Tango database:
- Connection
- Configuration

## Slide 5
Mirrored
Disk array
Display layer (15 hosts)
Linux worstations
few Windows PC
Process layer (20 hosts)
Solaris + Linux servers (aries,etc…)
Windows servers
Hardware control layer (110 hosts)
VME, PCs,
Linux, Windows
Field layer Fbus, Serial lines, dedicated systems
Wago, G64, Liberas, PLC…
Disk
server
Accelerator Control System Layers

## Slide 6
Network infrastructure
CTRM network
Routers
WiFi network
Technical gallerie
technical network
technical network
technical network
technical networks
Router
Rest of the
world
Firewall
Rest of the ESRF
Accelerator Control System

## Slide 7
Accelerator
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
beamline
Control system
requests
One large system
40 small systems
Read parameters
Control insertion devices
Opening/closing frontend
Accelerator – Beamline CS

## Slide 8
We started in the beginning of the nineties with TACO (Telescope and Accelerator Control Object), a device oriented control system.
Taco allows to have classes in C (and later in C++).
TACO / TANGO
Learn from imperfections and limitation
TANGO development (TACO New Generation Object), a new device oriented control system based on CORBA.
It is a Object oriented software. It allows to have classes in C++, Java and Python.

## Slide 9
Main improvements with TANGO:
  Attributes are auto describing (description, label, units,…)
  Tango manage attribute polling, with time stamping and an history buffer.
  Tango allows 3 modes of communication:
    Synchronous calls
    Asynchronous calls
    Events (on period, on change, and for archive)
  Tango allows to use high level language (Java and Python) for GUI.
TANGO Control System
Tango proposes:
  A set of management tools (Astor/Starter).
  A Database browser (Jive)
  A class generator (Pogo)
  Generic tools (ATK viewer, ATKpanel) using auto-description.
Tango is developed incollaboration with:
  Soleil (France)
  Elettra (Italy)
  Alba (Spain)
  Petra III at Desy (Germany)
  Max IV (Sweden).

## Slide 10
1 Device can also interface complex systems
  Hierarchical structure
TANGO Software Bus
Client
Macro device: e.g. Accelerator
sub devices: e.g. powersupplies
sub devices: e.g. ADC, modbus…
Client
TANGO Devices

## Slide 11
Main Problem:
All device servers cannot be re-written in TANGO in few days.
It takes years and we need to support TACO and TANGO on accelerator.
TACO / TANGO

## Slide 12
5 years ago we start to move vacuum control to Tango to:
  Do diagnostics on vacuum:
    Display info about 700 pressures and 900 temperatures, 25 RGAs.
    An historic buffer:
    Use Tango polling on attribute (1 second) with a buffer depth of 1 hour.
    Quick view on problem if any.
    Foreseen possible problem coming soon.
  Write pressures in HDB with complex criteria:
    Use Tango polling on pressure attribute to compute criteria and send data to HdbAccess (Taco HDB) Tango device server if needed.
Vacuum Control System
Now we are moving to a complete Tango vacuum control:
  All vacuum servers must be Tango servers.
  SrVac and SyVac applications must be re-written as Tango clients.
  Install Tango vacuum servers on beamlines.

## Slide 13
Vacuum Control System
Taco server
Taco server
Taco server
Taco server
MultiCellGauges
Tango Spectrum Attributes
145 Tango servers
32 Servers
VacCellGauge
Tango Scalar Attributes
Tango Spectrum
Attributes and
History
Taco Tango Pressures principle:
- 1 server for the storage ring (MultiCellGauges) - 1 server for each cell (VacCellGauge) - 1 server for 4or 6 physical devices (VacGauge)
VacCellGauge
VacCellGauge
VacGauge
Serial line
VIP
Serial class
Pump
Pump
Controller
VacGauge
Serial line
VIP
Serial class
Pump
Pump
Controller
VacGauge
Serial line
Balzers
Serial class
Gauge
Gauge
Controller
VacGauge
Serial line
Balzers
Serial class
Gauge
Gauge
Controller
~ 100 Balzers Taco servers
~ 150 VIP Taco servers

## Slide 14
Vacuum Control System
VacGaugeServer
Tango server
BalzerGauge
Class
VacGauge Class
BalzerTpg300
Class
VarianIP
Class
VarianCtrl
Class
Serial
Class
Store data in HDB
Attributes (Pen or IP) are:
  Pressures
  MaxPressure
  DerivativePressure
  State
Device names are:
  domain / v-pen /member
  domain / v-ip / member
Models a Varian ion pump
Attributes are:
  Pressures
  Voltage
  n Step Current
  State
Commands: ON, OFF
Device names are:
  domain / v-varip /member
Models a Baglzers gauge
Attributes are:
  Pressures
  State
Commands: ON, OFF
Device names are:
  domain / v-balzpen /member
The Tango device server “VacGaugeServer”

## Slide 15
Vacuum Control System
MultiCellGauges
Tango Spectrum Attributes
64 Tango servers
32 Servers
VacCellGauge
Tango Scalar Attributes
Tango Spectrum
Attributes and
History
Pure Tango Pressures principle:
- 1 server for the storage ring (MultiCellGauges) - 1 server for each cell (VacCellGauge) - 1 server for pennings / cell
- 1 server for ion pumps / cell
VacCellGauge
VacCellGauge
VacGaugeServer Tango server
VacGauge
Serial line
Serial class
Pump
Pump
Controller
VarianCtrl
VarianIP
VacGauge
Serial line
Serial class
Pump
Pump
Controller
VarianCtrl
VarianIP
VacGaugeServer Tango server
VacGauge
Serial line
Serial class
Gauge
Gauge
Controller
BalzersTPG
BalzersGauge
VacGauge
Serial line
Serial class
Gauge
Gauge
Controller
BalzersTPG
BalzersGauge

## Slide 16
Vacuum Control System
For Booster.
For Storage Ring after winter shutdown.

## Slide 17
Vacuum Control System
For Booster.
For Storage Ring after winter shutdown.

## Slide 18
Vacuum Control System
Add a pump

## Slide 19
Vacuum Control System
On beamlines (installation phase on ID08).

## Slide 20
Vacuum Control System
New diagnostics

## Slide 21
ESRF Vacuum Control System
Pascal Verdier
ISDD software group
4th of October 2010
New Vacuum Application
New Vacuum Servers
How to manage servers

## Slide 22
Vacuum Control System

## Slide 23
Vacuum Control System
Tango manager tool : Astor (combined with Starter device servers)

## Slide 24
Vacuum Control System

## Slide 25
Vacuum Control System
MultiCellGauges
Tango Spectrum Attributes
64 Tango servers
32 Servers
VacCellGauge
Tango Scalar Attributes
Tango Spectrum
Attributes and
History
Pure Tango Pressures principle:
- 1 server for the storage ring (MultiCellGauges) - 1 server for each cell (VacCellGauge) - 1 server for pennings / cell
- 1 server for ion pumps / cell
VacCellGauge
VacCellGauge
VacGaugeServer Tango server
VacGauge
Serial line
Serial class
Pump
Pump
Controller
VarianCtrl
VarianIP
VacGauge
Serial line
Serial class
Pump
Pump
Controller
VarianCtrl
VarianIP
VacGaugeServer Tango server
VacGauge
Serial line
Serial class
Gauge
Gauge
Controller
BalzersTPG
BalzersGauge
VacGauge
Serial line
Serial class
Gauge
Gauge
Controller
BalzersTPG
BalzersGauge

## Slide 26
Vacuum Control System

## Slide 27
Vacuum Control System
For Booster since summer shutdown.

## Slide 28
Vacuum Control System
For Storage Ring after winter shutdown.

## Slide 29
Vacuum Control System
Find a device server.

## Slide 30
Thank you!